## Slide 1
Buffer Size; Pipeline_core & Pipeline_alloc; Pipeline_links with peek Router
Modifications of CONNECT(beta version)
3 Modifications by 10/05/2015
5 Modifications by 06/22/2016
RoundRobin Arbiter; Virtual Link with pipeline option; Virtual link in IQ_credit Router; Virtual link in VOQ router; VC router with pipeline_alloc
6/22/2016

## Slide 2
00
01
10
11
Buffer Size 4
2 bits
head
tail
‘11’ + ‘1’ = ‘00’
(new_tail == head) -> full
000
001
010
011
Buffer Size 5
3 bits
head
tail
‘100’ + ‘1’ = ‘101’
(new_tail != head) -> not full
100
101
(‘100’ + ‘1’) % fifo_depth = ‘101’ % ‘101’ = ‘000’
1 Buffer Size
Description: when buffer size is not power 2, some flits are misallocated
Modification: Need modulo operation when updating new_tail
Files Modified: MultiFIFOMem.bsv

## Slide 3
2 Pipeline_core & Pipeline_alloc
Description: when enable pipeline_core or pipeline_alloc option, some flits are misallocated
Modification: When generate the deq signal of the flitbuffer, double check the ourPortFIFOs_first with selectedOut.valid to make sure it’s sending the flit to the right port. If they are not equal, then wait for next try. That’s the idea of speculative pipeline.
Files Modified: Router.bsv; RouterSimple.bsv; IQRouter.bsv; IQRouterSimple.bsv; VOQRouterSimple.bsv

## Slide 4
3 Pipeline_links with Peek Router
Description: when enable pipeline_links option, and use peek flow control, some flits will be enqueued to full FIFO
Modification: Set the margin of flit buffer 2 instead of 1. Modify the dynamic assertion to avoid unnecessary warning(More details next slide)
Files Modified: RouterSimple.bsv; IQRouterSimple.bsv; MultiFIFOMem.bsv

## Slide 5
Router 0
Router 1
flit
Not full
Modification :
Step1. In RouterSimple.bsv and IQRouterSimple, the margin of flit buffer should be 2 instead of 1. Because both flit and not full signal has one cycle delay across the link. So when the flit buffer in Router 1 is almost full, it should indicate router 0 two cycles before it’s really full.
Step2. In MultiFIFOMem.bsv, we should use “real full” instead of “almost full” signal for the bluespec dynamic assertion. Because when the flit buffer is almost full, the on-fly flit can still be enqueued into this buffer.
Step3. In previous design, when there is a deq, the buffer becomes not full. However, things are different when we introduce margin, because we are actually using “almost full” to inform other router. When we update the new_head, we should be careful about the distance between cur_tail and new_head. If the distance is less than the margin, we should still say the buffer is “almost full”.
pipeline
3 Pipeline_links with Peek Router(con’t)

## Slide 6
4 RoundRobin Arbiter
Description: The “RoundRobin” Arbiter in CONNECT is actually Oblivious Arbiter from PPIN by Bill Dally. (I change it into the RoundRobin Arbiter described by PPIN for comparison with my HLS NoC. And RoundRobin can be more fair than Oblivious Arbiter.)
Modification: Update the “token” based on the “winner” instead of letting “token” update itself independently. In allocators.bsv, choose mkRoundRobinArbiter instead of mkRoundRobinArbiterStartAt.
Files Modified: Arbiters.bsv; Allocators.bsv

## Slide 7
5 Virtual Link with pipeline option
Description: When enable pipeline option and virtual link option, the node would receive uncontinuous flits while supposed to receive continuous flits from one packet.
Modification: Need to double check the lock states when enable the pipeline option. Otherwise the deq signals of flit_buffer would be generated based on stale lock info.
Files Modified: Router.bsv; RouterSimple.bsv; IQRouter.bsv; IQRouterSimple.bsv; VOQRouterSimple.bsv

## Slide 8
6 Virtual link in IQ_credit Router
Description: For the IQ_credit Router, when enable virtual link, the node would receive uncontinuous flits while supposed to receive continuous flits from one packet
Modification: It seems like a copy-paste error. The lock states(lockedVL inPortVL) are not updated. Copy the updating code from other router code.
Files Modified: IQRouter.bsv

## Slide 9
7 Virtual link in VOQ Router
Description: For the VOQ Router, when enable virtual link, the router would unnecessarily stop sending eligible flits
Modification:When generate eligIO, no need to do “eligIO[i] = replicate(False)” before “eligIO[i][o] = True”. If we do that, that means the highest ‘o’ has highest priority. But we do not need to set this priority. For VOQ router, it’s possible for one inport to generate requests to multiple outport. This is different from IQ and VC(for VC actually we can, but we choose to set a static priority). The multiple request from one inport can be allocated by the separable allocator. Files Modified: VOQRouterSimple.bsv

## Slide 10
8 VC router with pipeline_alloc
Description: For the VC Routers, enabling pipeline_alloc will result more speculative penalty compared with enabling pipeline_core
Modification: When enable pipeline_core in VC router, the sel_VC will be latched. While enabling pipeline_alloc, the sel_VC will not be latched. That would result more speculative penalty because the sel_VC comes from the current first element flit vc, not the vc for the granted flit.
Files Modified: Router.bsv; RouterSimple.bsv